InnoMedia ESBC

Checklist for Voice Service Deployment

This check list is service provider centric. Reviewing the following topics before proceeding the voice service deployment to enterprises.

SW 2.0.13.0

June, 2014

Table of Contents

InnoMedia ESBC	1

1	SIP Trunking Service	4

1.1	ESBC- North Bound Configurations, to the Service Provider Network	4

1.1.1	WAN connections	4

1.1.2	Capacity requirements	4

1.1.3	SIP Trunk	4

1.1.4	Public Identities / DIDs	5

1.1.5	SIP signaling interworking and normalization	5

1.1.6	Media Interworking/transcoding with the service provider network	5

1.1.7	Security/fraud protection	6

1.1.8	Operation and Management	6

1.1.9	North bound call reachability and voice quality confirmation	7

1.2	ESBC – South Bound Configurations, to the SIP PBX	7

1.2.1	Enterprise Voice Network Arrangement	7

1.2.2	SIP signaling interworking	8

1.2.3	Media Interworking/Transcoding	8

1.2.4	Security/fraud protection	9

1.2.5	SIP-PBX configuration steps	9

1.3	ESBC – South Bound Configurations, to the TDM-PBX	10

1.3.1	Identifying ISDN PRI Type (product models)	10

1.3.2	Identifying the TDM-PBX model/brand	10

1.3.3	Identifying the Basic Settings of ISDN parameters	10

1.3.4	ISDN Interoperability Settings	11

1.3.5	Call reachability and voice quality confirmation	12

1.3.6	TDM-PBX configuration steps	13

2	Hosted Voice Service	14

2.1.1	WAN connections:	14

2.1.2	Concurrent calls requirements	14

2.1.3	SIP UAs at the LAN side	14

2.1.4	SIP Message Interworking:	14

2.1.5	Security/fraud protection	15

2.1.6	Call reachability and voice quality confirmation	15

3	Location and How	16

List of Figures

Figure 1. SIP UA Settings-DID Number Configuration	16

Figure 2. SIP UA Settings with Default Route Configuration	16

Figure 3. Caller ID display for outgoing calls	17

Figure 4. Security Features to verify incoming SIP messages	17

Figure 5. SIP Firewall Rules	18

Figure 6. Network time server synchronization	18

Figure 7. Embedded SIP UA, Test Agent, to confirm voice reachability and quality	19

Figure 8. Voice Quality Matrix and SLA	19

Figure 9. SNMP Trap configurations	20

Figure 10. the ESBC Alert Notifications	20

Figure 11. SIP-PBX Profile Selection and Configurations	21

Figure 12. Configuring registration agent on the ESBC for IMS implicit registration	21

Figure 13. SIP Method Filtering	22

Figure 14. Media activity timer	22

Figure 15. Span Setting Screen—Basic	22

Figure 16. PRI Settings: Interoperability	23

Figure 17. PRI Settings: Ring back tone or early media settings for outbound calls	23

# SIP Trunking Service

## ESBC- North Bound Configurations, to the Service Provider Network

### WAN connections

| Component | Customer Value | Comments |
| --- | --- | --- |
| Broadband access method |  | Fiber/Cable/ADSL/… |
| Internet connection |  | Public internet (bring your own broadband) , or Private (managed) network |
| Bandwidth allocated for SIP Trunk service |  |  |
| DNS server |  | Is the DNS used by the voice service provider different from that from the ISP? |
| Cable Modem integrated with the ESBC |  | Yes/No? Policy Server? DOCSIS/EuroDOCSIS? DOCSIS 2 / DOCSIS 3? |
| QoS preference |  | VLAN or ToS |

### Capacity requirements

| Component | Customer Value | Comments |
| --- | --- | --- |
| Concurrent calls/ trunk number requirements |  | System capacity of the deployed site. (Trunk/users percentage) The number of concurrent calls) requirement should be on the full utilization of the expected number of agents and sufficient trunks for the expected number of waiting callers. (erlang numbers) |

### SIP Trunk

| Component | Customer Value | Comments |
| --- | --- | --- |
| SIP Server: vendor/model |  | Is IMS? |
| SBC vendor/model |  |  |
| SIP Proxy Outbound Proxy SIP Domain Port |  | SIP Trunk setting information: List parameters needed for Trunk profile settings. |
| SIP signaling needs encryption? |  | TLS CA root certificate required? |
| Redundant SIP Servers |  | Yes/No? By DNS lookup (NAPTR-SRV-A Record) or server list table |

### Public Identities / DIDs

| Component | Customer Value | Comments |
| --- | --- | --- |
| IMS implicit registration. (Registration Agent) |  | Registering the pilot number (main trunk number) on behalf of all IMPUs. Location and How. |
| SIP UA (Public Identity) Configurations |  | SIP Account IDs and Password (Auth ID?) Configuring the main public identity (whether default route needed?) Alternate public identity (DID numbers) Location and How |
| Caller ID display for outgoing calls |  | From the original caller (PBX) or from the public identities configured on the ESBC. Location and How |
| Number globalization |  | Prefixed with plus sign. |
| Numbering plan |  | Digit translation needed with the PBX |

### SIP signaling interworking and normalization

| Component | Customer Value | Comments |
| --- | --- | --- |
| Billing preference |  | “call transfer” and “call forwarding” in terms of SIP methods: REFER/302 vs. reINVITE. (after call features being processed, whether lines are still billed?) Place calls among the configured SIP UAs as internal calls |
| SIP Registration or Static operation mode. |  | If static mode, the ESBC has to have fixed IP address on the WAN interface which the SIP Proxy server uses for authentication and call connections. |
| Use of early media requirement |  | Outbound calls required 100rel reliable provisional response support? Always respond with PRACK for 183? Location and How |
| Use of ring back tone |  | Determine play RBT until 18x response from the SIP server; or play RBT immediately required? |
| Determining appropriate URI format of header |  | E.164 and/or user=phone |
| Applying SIP Header Manipulation rules needed? |  | Only needed if there are exceptional IOT requirements. Example: The caller ID filtering (and manipulation) for the diversion headers due to call forwarded from the PBX. (authentication requirements on the SIP proxy server side. |

### Media Interworking/transcoding with the service provider network

| Component | Customer Value | Comments |
| --- | --- | --- |
| Voice Codec used |  | Codec filtering for bandwidth control or assuring voice-experience quality |
| DTMF |  | Inband or Out-of-band (RFC 2833, SIP INFO) Payload type assignments of RFC2833 |
| FAX: T.38 / Passthrough |  | Allowing T.38 (can fallback to pass-through)? Or Pass-through only? Using the ESBC FXS ports for FAX? |
| Maintaining fax calls on business lines |  | using the ESBC FXS port for fax transmission? |
| Maintaining modem calls on business lines |  | Such as credit card reader. (using the ESBC FXS port?) |
| Media activity timer |  | Location and How |

### Security/fraud protection

| Component: SIP Application Layer Protection | Customer Value | Comments |
| --- | --- | --- |
| SIP firewall rules. Only process SIP requests from friendly IP address. Drop all others. |  | If the deployment is on the public internet. It is recommended to apply applying sip firewall rules. Location and How |
| Verify incoming SIP messages: check domain |  | Location and How |
| Verify incoming SIP messages: check the source IP address of incoming SIP messages. |  | Only the service provider, SIP Proxy or SBC, can initiate calls to the ESBC from within the PSTN side. Location and How |
| Component: IP Layer Protection | Customer Value | Comments |
| IP Layer Protection. ACL. |  | Drop/Deny all access attempts from any hosts if not in the legitimate list. |

### Operation and Management

| Component | Customer Value | Comments |
| --- | --- | --- |
| Auto-provisioning for subscribed service |  | Provisioning protocol, Provisioning ID/PW and encryption key. |
| Administrator/Technician ID and password |  | Needing to define the manufacture default values? |
| Network time server selection and synchronization |  | System time synchronization Location and How |
| Time zone/DST settings |  |  |
| EMS server configuration |  | Collecting CDR, VQM, Alerts Management |
| Operational syslog server |  | Optional. Syslog server IP address |
| System configuration auto backup |  | Optional. ftp IP address |

### North bound call reachability and voice quality confirmation

| Component | Customer Value | Comments |
| --- | --- | --- |
| Test Agent Call Control |  | By the ESBC embedded SIP UA (test agent) to make calls to a specified number. To verify calls reachability and voice quality, in both automatic/periodic and manual manners. Location and How |
| Component: | Customer Value | Comments |
| Run time VQM |  | Continuous monitoring the voice quality of SIP trunk service. Location and How |

## ESBC – South Bound Configurations, to the SIP PBX

### Enterprise Voice Network Arrangement

| Component | Customer Value | Comments |
| --- | --- | --- |
| InnoMedia ESBC |  |
| ESBC LAN (VoIP Port) IP Address |  |  |
| ESBC LAN (VoIP Port) subnet mask |  |  |
| ESBC LAN (Management Port) IP Address |  | Optional. If the management port is used on the ESBC, the administrator can logon to ESBC WEB GUI / CLI console via the management port but not the VoIP port. The administrator PC has to be on the same subnet of the management port. |
| ESBC LAN (Management Port) subnet mask |  |  |
| Static routing table |  | Optional. Only needed when the SIP UAs are scattered among multiple subnets. |
| RTP Default Gateway |  | Optional. Only needed when the SIP UAs are scattered among multiple subnets, and the ESBC static routing table cannot be maintained, it is recommended to identify a default gateway (router) for these SIP UAs to route voice traffic to the ESBC. |
| SIP-PBX |  |
| IP Address of SIP-PBX |  | This IP address of SIP-PBX is typically on the same subnet of the ESBC LAN. If it is not, the static routing table must be configured on the ESBC. |
| Network subnet mask |  |  |
| Network default gateway |  |  |
| DNS |  | Optional. The DNS server for the enterprise network. If FQDN is used for connecting to the ESBC VoIP interface rather than using the IP address, the DNS should be configured on the SIP-PBX. |

### SIP signaling interworking

| Component | Customer Value | Comments |
| --- | --- | --- |
| InnoMedia ESBC |  |
| Identify the SIP-PBX model and choose the target SIP-PBX profile. |  | There are SIP-PBX profiles created for different SIP-PBX models. These profiles include appropriate sip parameter values used to connect to the specified SIP PBX. Unless necessary, no need to configure these values. If your SIP-PBX model is not in the list, use “generic” profile. Location and How |
| SIP-PBX IP address or FQDN |  | Only when the SIP-PBX uses static register mode to connect to the ESBC, the ESBC needs this value for SIP Contact (e.g., user@pbx-fqdn:port). |
| PBX SIP Authentication required? Password. |  | If Authentication is enabled, and it is Local. Password = sip UA auth password of SIP Trunk. Radius. Password = user defined password. |
| Numbering plan with the SIP-PBX |  | Digit translation required? |
| SIP-PBX |  |
| SIP UA Registration to the ESBC |  | Depending on subscribed service, the SIP-PBX may use “main public identity” or all “alternative public identities” (DID) to register to the ESBC. |
| Filtering SIP Methods |  | Configuring SIP methods to/from the SIP PBX. Location and How. |
| SIP Header Normalization Rules needed? |  | Only needed when there are exceptional IOT requirements. (for example, number globalization + sign, number filtering, or SIP message translations.) |

### Media Interworking/Transcoding

| Component | Customer Value | Comments |
| --- | --- | --- |
| InnoMedia ESBC |  |
| FAX |  | Are there FAX/VoIP gateways connecting to the SIP-PBX or the FAX machines connecting to the FXS ports of the SIP-PBX? T.38 or Pass-through |
| DTMF processing |  | Inband, or Out-of-band (2833, or SIP INFO) |

### Security/fraud protection

| Component: SIP Application Layer Protection | Customer Value | Comments |
| --- | --- | --- |
| White list. Only process SIP requests from friendly IP address. |  | Applying sip firewall rules |
| Component: IP Layer Protection | Customer Value | Comments |
| IP Layer Protection. ACL. |  | Drop/Deny all access attempts from any hosts if not in the legitimate list. |

### SIP-PBX configuration steps

Referring to the ESBC application notes with your target SIP-PBX models.

## ESBC – South Bound Configurations, to the TDM-PBX

### Identifying ISDN PRI Type (product models)

- E1 or T1

### Identifying the TDM-PBX model/brand

### Identifying and configuring the Settings of ISDN parameters

| TDM Basic Settings | Customer Value | Description. Span Setting Screen—Basic |
| --- | --- | --- |
| Enabling Span |  | Span 1 should always be enabled. (Span can be disabled) |
| Clock Mode |  | Internal/Line. The default clock mode is “Internal” with which the ESBC follows own clocking scheme, and the TDM PBX should follow the ESBC clock. |
| Line Framing/Coding |  | T1 / J1: ESF/B8ZS or D4/AMI E1: CCS/HDB3 or CCS/HDB3 CRC4 The configuration of ESBC should match that of the TDM-PBX. |
| Line Build Out |  | The physical distance between the ESBC and TDM-PBX. Default 0 db (CSU) / 0-133 feet (DSX-1). The configuration of ESBC should match that of the TDM-PBX. |
| Enabling B Channel numbers |  | Total channel numbers per span: T1-24 channels; E1-31 channels B-Channel: configuring the enabled B-channel numbers. (Note that TDM-PBX may not have all B channel enabled) D-Channel: T1 fixed at CH 24; E1 fixed at CH 16 |
| Switch Type |  | T1: National ISDN 2 (default), Nortel DMS100, AT&T 4ESS, Lucent 5ESS, Old National ISDN 1, Q.SIG E1: EuroISDN (common in Europe) The configuration of ESBC should match that of the TDM-PBX. |
| Signaling method |  | PRI NET/PRI CPE. Configuring the ESBC with the PRI NET mode to perform switch functionality, and configuring the TDM-PBX with the CPE mode. (Do not change the mode unless necessary) |

### ISDN Interoperability Settings

| TDM Interworking Settings | Customer Value | Description. PRI Settings: Interoperability |
| --- | --- | --- |
| Enable Call Transfer / Call forwarding (Billing preference) |  | ISDN supplementary services: (Two B Channel Transfer, or Release Link Trunk, or Explicit Call Transfer) National ISDN II-TBCT/Nortel DMS-RLT/Euro ISDN-ECT. When enabled, the ESBC uses SIP REFER/302 method to the SIP Server side for call transfer/forwarding operations. (The setting should be matching to the billing preference at SIP signaling interworking and normalization) |
| PRI Cause Code-SIP Response Code mapping |  | Configuring special PRI Cause Codes vs. SIP Response Codes, or vice versa. (No need to configure the settings unless necessary) |

| Ring back tone (or early media) requirements for outbound calls |  | Description. PRI Settings: Ring back tone or early media settings for outbound calls |
| --- | --- | --- |
| Does the core network sends 180 SIP response code and expects premises equipment to process RBT process locally? |  | Play RBT for outgoing calls ALWAYS: The ESBC always sends inband RBT or early media to the PBX, either generating locally or from the network. NEVER: the ESBC never generates inband RBT locally but forwards inband RBT or early media from the network. AS-NEEDED. The ESBC process RBT according to signals received (SIP messages from the network and Q.931 PI codes from TDM-PBX). Ignore 183 early media (optional) |
| Does the core network sends 183 SIP response code and inband RBT or early media before callee answering? |  |  |
| (A) Is the TDM-PBX able to play inband RBT or early media from the switch side? (B) Or does the TDM-PBX always play RBT locally and cannot play inband RBT? |  |  |

| Early Media requirements for inbound calls |  | Please referring to the ESBC Administrative Guide for detailed. Configurable options available on the ESBC |
| --- | --- | --- |
| Is the TDM-PBX able to process inband RBT or early media for inbound calls? |  | Enabling early media for inbound calls. |

### Call reachability and voice quality confirmation

| Component | Customer Value | Comments |
| --- | --- | --- |
| Test Agent Call Control |  | By the ESBC embedded SIP UA (test agent) to make calls to a specified number. To verify calls reachability and voice quality, in both automatic/periodic and manual manners. Location and How |
| Component: | Customer Value | Comments |
| Run time VQM |  | Continuous monitoring the voice quality of SIP trunk service. Location and How |

# Hosted Voice Service

### WAN connections:

| Component | Customer Value | Comments |
| --- | --- | --- |
| Broadband access method |  | Fiber/Cable/ADSL/… |
| Internet connection |  | Public internet (bring your own broadband) , or Private (managed) network |
| Bandwidth allocated for voice service |  |  |
| Cable Modem integrated with the ESBC |  | Yes/No? Policy Server? DOCSIS/EuroDOCSIS? DOCSIS 2 / DOCSIS 3 ? |
| QoS preference |  | VLAN or ToS |

### Concurrent calls requirements

| Component | Customer Value | Comments |
| --- | --- | --- |
| Concurrent calls/number of SIP UAs |  | System capacity of the deployed site. The number of concurrent calls requirement should be on the full utilization of the expected number of SIP UAs and erlang numbers. |

### SIP UAs at the LAN side

| Component | Customer Value | Comments |
| --- | --- | --- |
| SIP UAs: methods of obtaining IP address |  | Obtaining IP address from the ESBC, or the fixed IP. (the default gateway has to point to the ESBC LAN) |
| SIP device vendors/models |  |  |
| DNS server IP address |  | Is the DNS used by the voice service provider different from that from the ISP? |
| Static FQDN-IP table for the outbound proxy configured on the SIP UAs? |  | Only needed when the outbound proxy from the SIP UAs cannot be resolved by the DNS server configured. |
| Static FQDN-IP table for SIP domain on the SIP UA? |  | Only needed when the outbound proxy from the SIP UAs cannot be resolved by the DNS server configured. |

Note: The ESBC determines the IP of SIP requests to service provider network based on (1) DNS static records, (2) DNS cache (3) issuing a DNS query, in sequence.

### SIP Message Interworking:

| Component | Customer Value | Comments |
| --- | --- | --- |
| Applying SIP Header Manipulation rules needed? |  | Only needed if there are exceptional IOT requirements. Examples: Should stripe ICE attributes? Should change the SIP response codes? Privacy settings |

### Security/fraud protection

| Component: SIP Application Layer Protection | Customer Value | Comments |
| --- | --- | --- |
| White list. Only process SIP requests from friendly IP address. |  | Sip firewall rules |
| Component: IP Layer Protection | Customer Value | Comments |
| IP Layer Protection. ACL. |  | Drop/Deny all access attempts from any hosts if not in the legitimate list. |

### Call reachability and voice quality confirmation

| Component | Customer Value | Comments |
| --- | --- | --- |
| Test Agent Call Control |  | By the ESBC embedded SIP UA (test agent) to make calls to a specified number. To verify calls reachability and voice quality, in both automatic/periodic and manual manners. Location and How |
| Component: | Customer Value | Comments |
| Run time VQM |  | Continuous monitoring the voice quality of the hosted voice service. Location and How |

# Location and How

Main Public Identity and Alternate Public Identities (DID Numbers)

Depending on the TNs or DID Numbers subscribed, the ESBC could be configured by entering all accounts; or in a simpler manner, Default Route Option can be used so that the Main Trunk Number can be configured on behalf of all TNs or DID Numbers.  Hence, the ESBC process all TNs or DID numbers which belong to same PBX (SIP or TDM) following the Default Route settings. If the DIDs are assigned to other SIP entities or PBX, they must be configured on the ESBC individually.

Figure 1. SIP UA Settings-DID Number Configuration

Figure 2. SIP UA Settings with Default Route Configuration

Caller ID Display for Outgoing Calls

For outgoing calls to the network side, the ESBC can be configured to send either the Main Trunk Number (Main Public Identity), Original Caller, or the Alternate Identity.  The ESBC will manipulate the From: Header to use either of the options set.

Figure 3. Caller ID display for outgoing calls

Play Ringback until receive 18x response from SIP Server

18x message may not be delivered to the ESBC from the SIP Server when placing outgoing calls due to server processing or network delays or other issues. By checking this option, the ESBC plays the ringback tone to the PBX before the 18x message is received from the SIP Server.

Security features to verify incoming SIP Messages

The security features verify and check the incoming SIP messages to ensure it is originated from the configured call agent in the Trunk Settings.  At the same time, the domain and host of the To header are verified before passing the SIP message to the PBX.

Figure 4. Security Features to verify incoming SIP messages

SIP Firewall Rules

The SIP Firewall script rules are created and used to drop or reject any SIP messages that are not originated from IPs or networks in the white list.  The SIP messages will not be responded to if they are dropped.  This will prevent any SIP hacker from establishing any DOS attacks or any theft of service.

Figure 5. SIP Firewall Rules

ESBC System Time Synchronization with Network Time Server

The ESBC system time must synchronize with network time for accurate accounting, and related managerial, or trouble-shooting purposes, such as Syslog, voice quality, SNMP Event Messages.

Figure 6. Network time server synchronization

Test Agent: reachability and voice quality

Figure 7. Embedded SIP UA, Test Agent, to confirm voice reachability and quality

Run time Voice Quality

To ensure an SLA (Service Level Agreement) with the enterprise customer, the ESBC provides a Voice Quality measurement tool to calculate the MOS scores of every call.  These measurements can be sent to a Syslog Server or an EMS Server for further analysis.  Traps can also be sent out when the threshold falls below a certain MOS score.

Figure 8. Voice Quality Matrix and SLA

SNMP Traps and Alert Notifications

The ESBC can report traps and alerts in real time to an external server.  Several alert notifications can be sent during any errors such as registration failures, LAN Interface down, voice quality below thresholds, etc.

Figure 9. SNMP Trap configurations

Figure 10. the ESBC Alert Notifications

PBX Profile Selection and Configurations

To ensure interoperability with the enterprise customer’s PBX, the ESBC can be configured to high level profile settings.  These settings are pre-configured cased on interoperability testing.  Lower level configurations can be made within the profile.

Figure 11. SIP-PBX Profile Selection and Configurations

Registration Agent

IMS defines “implicit registration” to have the pilot number (or main trunk number) to perform registration and subscribe services for all public identities of a service profile to the IMS servers.

Figure 12. Configuring registration agent on the ESBC for IMS implicit registration

Filter SIP Methods to/from the IP-PBX

Some SIP Methods may not be allowed or supported on either the Service Provider’s SIP Server or on the customer’s IP-PBX.  The ESBC can be configured to disallow any SIP Methods that are not supported on either side.

Figure 13. SIP Method Filtering

Media Inactivity Timer

SIP messages may get lost in the network causing sessions to stay active within the ESBC.  The Media Inactivity Timer may be enabled to drop any session for a configured time period that may not have any RTP Session.

Figure 14. Media activity timer

PRI Span Settings: Basic

Figure 15. Span Setting Screen—Basic

PRI Span Settings: Interoperability

Figure 16. PRI Settings: Interoperability

PRI Span Settings: ring back tone and early media

The ringback tone options on the ESBC must be configured appropriately to ensure correct expectations of ringback generation.  The ESBC can be configured to always send ringback, have it originate from the network side, or have the TDM PBX to generate the ringback locally.  If the network side sends 183 Early Media messages, it can be ignored by the ESBC so that the ringback can be provided by the ESBC or the TDM PBX.

Figure 17. PRI Settings: Ring back tone or early media settings for outbound calls